## Slide 1: CS3220 Processor Design
Spring 2017
Prof. Hyesoon Kim

## Slide 2: Project #3: fmeidan2.mif execution time

## Slide 3: Project #4

## Slide 4: Better Devices
Now SW, KEY can be read
  Problem: several instructions needed to detect change
A better input device e.g. SW
  Have the usual 10 data bits (what we have now)
  Add status bits
    A “ready” bit to tell us if there has been a change in data
      Set to 1 automatically when any SW changes value
      Cleared to 0 when data is read
    An “overrun” bit to tell us if we missed something
      Set to 1 if SW changes value and Ready is already 1
      Cleared to 0
  Add control bits, such as Interrupt Enable (IE)
    If 1, Ready=1 causes interrupt request to processor
    We’ll have to figure out interrupts later, for now this bit has to be 0 

## Slide 5: Connecting Memory-Mapped Devices
We have a few devices
  Each with several memory-mapped registers (data, control, status, etc.)
All connected together using lots of if-statements
  Hard to make changes w/o creating bugs
  Hard to debug if there is a problem
Real systems can have 100s of devices
  Each with control, status, etc. registers
  The “if(dmemaddr==0xFFF0)…” approach is messy
We need a better way of connecting devices

## Slide 6: The Memory Bus
We read or we write at any given time
  Address, to know what is the location
  Data (either to or from memory/device)
  WE (says if we are reading or writing)
There are multiple entities attached
  Processor itself (it reads/writes data)
  Memory
  Key, sw, display, etc.
What goes on the address and WE wires?
  Easy – the processor always initiates an operation
  We say that the processor is the “bus master”
  It drives the address and WE signals, others just listen

## Slide 7: Another One Drives The Bus
But data wires are different
  If processor is writing, it drives the data lines
  If processor is reading, memory/device drives data
When does the processor drive the data bus?
  WrMem?DataToMem:Zs
When does memory drive the data bus?
  MemEnable is our “address is in the first 8kB” signal: (MemEnable&&!WrMem)?...
When does a device drive the data bus? ((memaddr_M==MyAddress)&&!WrMem)?...

## Slide 8: Putting it all together
wire [(DBITS-1):0] abus;
tri [(DBITS-1):0] dbus;
wire we;
// In the processor
assign abus=memaddr_M;
assign we=wrmem_M;
assign dbus=wrmem_M?wmemval_M:{DBITS{1'bz}};
// Attach some sort of a device
Timer #(.BITS(DBITS), .BASE(32'hF0000020), …) timer( .ABUS(abus),.DBUS(dbus),.WE(we), .INTR(intr_timer), .CLK(clk),.LOCK(lock),.INIT(init), .DEBUG()
);

## Slide 9: Bus interface in a device/memory
module Timer(ABUS,DBUS,WE,INTR,CLK,LOCK,INIT,DEBUG);
parameter BITS;
parameter BASE;
…
input wire [(BITS-1):0] ABUS;
inout wire [(BITS-1):0] DBUS;
input wire WE,CLK,LOCK,INIT;
output wire INTR;
…
wire selCtl=(ABUS==BASE);
wire wrCtl=WE&&selCtl;
wire rdCtl=(!WE)&&selCtl;
…
assign DBUS=rdCtl?{…Contents of the TCTL register…}:
rdCnt?{…Contents of the TCNT register…}:
{BITS{1'bz}};

## Slide 10: Practical issues
Must make sure only one entity drives the bus
  In our code, this is true at the end of each cycle
  But what happens during a cycle?

## Slide 11: But we don’t need that
Our bus wires are really just OR gates
assign DBUS=rdCtl?...:{BITS{1'bz}}; // In timer
assign DBUS=rdKey?...:{BITS{1'bz}}; // In keys
assign DBUS_t=rdCtl?...:{BITS{1'b0}}; // In timer
assign DBUS_k=rdKey?...:{BITS{1'b0}}; // In keys
assign DBUS=DBUS_t|DBUS_k|…;
Multiple drivers won’t damage our circuitry
If values correct (one driver) at end of cycle, when we get them into FFs, it’s all OK

## Slide 12: Devices
We will add “proper” devices for Project 4
  The KEY and SW get control and status registers
  The LEDR, HEX get read/write capability
    Lets us read what is being displayed
  Add a new programmable timer device
    Will let us do things that depend on real time
    E.g. we can do something exactly every 2 seconds
Interrupt support is optional in Project 4
And we’ll write a “X-max tree” application
  Same as Project 1, but this time it’s a program for our processor!

## Slide 13: KEY device
KDATA register at 0xFFFFF080
  Same as before
  Current state of KEY[3:0]
  Writes to these bits are ignored
KCTRL (control/status) register at 0xFFFFF084
  Bit 0 is the Ready bit
    Becomes 1 if change in KDATA state detected
    A read from KDATA changes it to 0
    Writes to this bit a re ignored
  Bit 1 is the Overrun bit
    Set to 1 if Ready bit still 1 when KDATA changes
    Writing a zero to this bit changes it to zero, writing a 1 is ignored
  Bit 4 is the IE bit
    If 0, KEY device does not generate interrupts
    Can be both read and written
  Start the device off with KCTRL all-zeros!

## Slide 14: SW device
SDATA register at 0xFFFFF090
  (Almost) the same as before
SCTRL (control/status) register at 0xFFFFF094
  Exact same bits as KCTRL, but these apply to SDATA
  Problem: if SW not debounced, will Overrun often
  Solution: SDATA holds debounced value
Debouncing SDATA
  Holds debounced value of SW (not raw SW value)
  SDATA changes only if the “raw” SW value is stable for at least 10ms
    E.g. if SW is 10’h000, changes to 10’h001, then 1ms later back to 0, SDATA just stays at 0 the whole time and the Ready bit does not change

## Slide 15: Debouncing Switches
Analog circuits:
  Add a filter
Digital circuits:
  Identify the initial value and check if the same value is exists for x cycles

## Slide 16: LEDR, HEX
Almost the same as before
  Writes to 0xFFFFF020 and 0xFFFFF000 change what is shown on HEX, and LEDR
    Only bits that actually exist are written
    E.g. writing value 0xFFFFFFFF to FFFF0020 is the same as writing 0x000003FF (LEDR only has 10 actual bits)
  But now reads from these addresses return what is currently shown
    Bits that “don’t exist” are returned as zero, e.g. after writing FFFFFFFF to LEDR, a read returns 0x000003FF

## Slide 17: New Device: Timer
TCNT at FFFFF100
  Read returns current value of the counter
  Write sets value of the counter
  Incremented every 1ms
TLIM at FFFFF104
  Write sets the value, read gets the value
  When TLIM is zero, it has no effect (counter just keeps counting)
  When TLIM!=0, it acts as the limit/target value for the counter
    If TCNT==TLIM-1 and we want to increment TCNT, we reset TCNT back to zero and set the ready bit (or overflow if Ready already set)
    If TLIM>0, the TCNT never actually becomes equal to TLIM (wraps from TLIM-1 to 0)
TCTL (control/status) register at FFFFF108
  Same bits as KCTRL and SCTRL
  “Ready” and Overflow bits set as described for TLIM
  Writing 0 to the Ready or Overflow bit changes it to 0, but writing 1 to one (or both) of these is ignored
    Properly written code should not write 1 to “Ready, but if it does then it has no effect
  Start the device off with TCNT, TLIM, TCTL all-zeros!

## Slide 18: Interrupts
Polling the devices to detect events is inefficient
  Processor kept very busy, but nothing actually done
We want to let devices interrupt the processor
  Processor can do whatever needs doing (e.g. sorting)
  When device needs attention, interrupt
  Processor executes interrupt handler to take care of device-related activity
  Processor returns back to whatever-needs-doing 
Each device has an IRQ signal assign IRQ = Ready && IE;
Processor’s IRQ signal = OR all device IRQs
  Interrupt the processor if any device wants to interrupt it 

## Slide 19: Interrupting the pipeline
Monitor the IRQ signal
  Normal execution continues if IRQ is 0
Save address of next instruction
  Where? Why not RA?
  Which instruction is “next”?
Indicate which interrupt was raised
  How?
Jump to interrupt handler routine
  Where is it?
  How to safely divert fetching?
  IRQ will still be 1, should not get stuck (forever doing the jump-to-interrupt thing)

## Slide 20: ISA Changes
Saving the return address
  Need a register for this (call it IRA)
  We have R11, R12 reserved for system use
    This is system use  so maybe we can use one of these
Where to jump on interrupts
  Simplest way – some low fixed address, e.g. 0x10 (this is below our program-start address at 0x100)
  Fancier way – address can be programmed
    Another register - IHA (interrupt handler address)
How do we know which interrupt we had?
  There could be many devices
  Each can have several interrupt-causing events

## Slide 21: Which interrupt?
Option 1: Handler checks each device
  Same handler for all interrupts
  Handler checks Ready bits of devices in priority order
Option 2: Different handler for each device/cause
  Separate handler for each device, no need to check
  Need many handler addresses
  Some devices very similar, could use the same handler
Option 3: Cause-ID number, pass it to handler
We’ll use the Cause-ID approach
  Put ID of interrupting device in a register, call it IDN (interrupt device number)

## Slide 22: Disable Interrupts?
Need some way to disable all interrupts
  Must disable all ints before we divert fetch to handler
    Why do we have to do this?
  Handler can enable ints again when it it’s safe
    When is it safe?
Typical approach
  Have a special control/status register PCS (processor control and status)
  Some bit (e.g. bit 0) is “Interrupt Enable” bit
  We’ll need a few more control/status bits soon

## Slide 23: Special Registers?
So far, we need four special registers
  And we have only R11, R12 reserved 
Must be automatically updated in HW
  This will create some tricky problems for our pipeline
  Regs written in last pipeline stage (let’s call it W), so on interrupt we must write them in the last stage
  But… that is three registers to write in one cycle!
  We really do not want to do that!
OK, write them one by one
  When taking interrupt, the last pre-interrupt instruction reaches the W stage
  The three cycles after that - update the IRA, IDN, and PCS registers
  Then we can do the first instruction of the interrupt handler
This is pretty messy
  Need some sort of a state machine for the three cycles, etc.

## Slide 24: Special Registers?
Plan B – Separate special registers
  We will have 4 extra registers for IRA, IHA, IDN, PCS
  Three of them written by hardware when int taken
But… how does our program read/write these
  Using special instructions, of course 
  RSR Rd,Ss – Read system register Ss (into Rd)
  WSR Sd,Rs – Write system register Sd (value from Rs)

## Slide 25: Interrupt handler code
IntHand:
; Save general purpose registers to stack
RSR A0,IDN ; Get cause of interrupt
; Decide what to do depending on A0
...
...
; Restore general-purpose registers from stack
...
; Return and enable interrupts
Which stack?
How?

## Slide 26: Saving Registers in Interrupt Handlers
Interrupt handlers need to use a stack
  Need to save *all* regs we modify
  Need to save IRA if we want to enable ints again
Can’t use the “normal” stack and SP for this!
  How much space does the app need for its stack?
  Is the app’s SP always in a usable state?
    SW RA,-4(SP) ADDI SP,SP,-4
    ADDI SP,SP,-4 SW RA,0(SP)
vs

## Slide 27: Need a separate SP
Idea: a separate SSP register
  This is what R11 and R12 are for
  So R11 is now SSP

## Slide 28: Interrupt handler code
IntHand:
; Save general purpose registers using SSP
ADDI SSP,SSP,-4 ; If only saving one reg
SW A0,0(SSP)
RSR A0,IDN ; Get cause of interrupt
; Decide what to do depending on A0
...
; Restore general-purpose registers
LW A0,0(SSP)
ADDI SSP,SSP,4
; Return and enable interrupts
???

## Slide 29: Returning from interrupt?
What needs to be done
  Enable interrupts
  Jump back to interrupted program
Let’s try this
  Enable interrupts (write to PCS)
  Use JAL to jump back
Problem 1: Need a register for JAL target
  Not a problem - can use R12 for this
    E.g. RSR R12,IRA, then JAL R12,0(R4)
Problem 2: New interrupt can come before JAL
  When it returns, R12 will be have the address of our JAL and we end up in an infinite loop (JAL to itself)
  Need to enable-interrupts-and-return (all at once)

## Slide 30: New instruction - RETI
Return from interrupt
  Jumps to address in IRA
  Enables interrupts (set IE to 1 in PCS)
Better: Restore IE to what it was
  Will come handy later (for non-maskable interrupts)
Add OIE (old-IE) bit to PCS
  When taking interrupt, IE copied to OIE, then set to 0
  RETI now copies OIE to IE
  What about nesting interrupts?
    Must save OIE before enabling interrupts in interrupt handler!

## Slide 31: Special register encoding
We can have up to 16 special regs in RSR/WSR
  We need only four of those:
  0: PCS (Processor Control/Status)
  1: IHA (Interrupt Handler address)
  2: IRA (Interrupt Return Address)
  3: IDN (Interrupt Device Number)
  4..15: Reserved

## Slide 32: Which address to save into IRA?
Option 1:
  Save pcgood from the stage that generates pcgood
  Flush all stages before that, set PC to IHA, start fetching from there
Option 2:
  Start fetch from IHA, let already-fetched insts finish
    Save pcgood when the last-fetched instruction produces it
    This happens a few cycles after fetch from IHA started
  Why would we want to do this?
    No wasted cycles
  Why would we not want to do this?
    More complex, and interrupts are taken rarely (OK to waste a few cycles)

## Slide 33: Be very careful with setting IRA
Say we produce pcgood in A stage
Say we get an int when a bubble-NOP in A
What will be saved into IRA?
  A bogus address produced by our bubble-NOP
Solution 1: Delay taking the interrupt
  Take int only if a “proper” inst in A
  The delay is at most a few cycles
Solution 2: Remember the last valid pcgood
  If bubble-NOP, use pcgood of last non-NOP inst!
Either way, we need to know if we have a bubble or not
  Have a bit for this purpose, set to 0 in decoding logic
  When NOP created by flush and stall, set this bit to 1

## Slide 34: Interrupt priority
Multiple devices may want to interrupt
  We will interrupt the processor
  But which ID to put in IDN?
OK, so we need some sort of priority
  We’ll use priority in order of IDs (0 is highest)
How to implement priority?
  Option 1: Daisy chain
  Option 2: Interrupt controller with priority

## Slide 35: Daisy chain
Each device has
  Input IRQ signal (from a lower-priority device)
  Output IRQ signal
  Connection to ID signal with tri-state logic
    Drive its own ID there only if no higher-priority device has IRQ=1
    But how do we know this?
  OK, se we need some signal (e.g. INTA) that goes back to lower-priority devices
  This is getting a bit too complicated for our purposes!

## Slide 36: Interrupt controller
Takes IRQ signal from each device
Outputs overall IRQ signal to the processor
  This is simply an OR of the incoming IRQ signals
Outputs the number of the “winner” device as ID
  Circuit that does this is called a “priority encoder”
  Processor puts this number into IDN when int taken

## Slide 37: Where is INTA from CS 2200?
Where is the INTA signal?
  We replaced it with software!
    Device keeps IRQ at 1 until handler does something!
  But now we must first remove the cause of the interrupt before we enable interrupts again!
    For the interrupt-causing device, set Ready bit to 0 (or set IE bit to 0)
  Otherwise, handler gets interrupted by the same interrupt cause as soon as it enables interrupts!

## Slide 38: Format of PCS
Which bit means what:
  Bit 0 is IE
  Bit 1 is OIE
What to do on interrupt/exception
  {OIE,IE}<={IE,1’b0}
What to do on RETI
  IE<=OIE

## Slide 39: Format for RSR, WSR, RETI
Option 1: Give each a new primary opcode
  But… they don’t need immed bits!
Option 2: Hijack one of existing instructions
  E.g. BEQ Rt,Rs,0 ordinarily makes no sense
    So we can declare that this is our RSR Rt,Ss
  Bad idea – breaks backward compatibility
    What is someone used BEQ R0,R0,0 in their code (makes no sense, but people can do things that don’t make sense)
Option 3: Use a secondary opcode in e.g. ALUR
  But… these are not ALU instructions…
Option 4: Create a new SYS primary opcode
  Then use secondary opcodes within that
  This is what we will do

## Slide 40: Format of new system instructions
Primary opcode for SYS is 6’h3F
RETI (opcode2 is 1)
{6’h3F, 8’h1, 18’b0}
RSR Rx, Sx (opcode2 is 2)
{6’h3F, 8’h2, rd, ss, 10’b0,}
WSR Sx, Rx (opcode2 is 3)
{6’h3F, 8’h3, sd, rs, 10’b0}
It’s your job to modify your assembler to handle these instructions and also decode them in your hardware.

## Slide 41: Where to read/write system registers?
Approach 1: Same as non-system registers
  Must take care of forwarding these values, too
  E.g. WRS followed by RSR in a five-stage pipeline
Approach 2: Like memory (R/W Sx in one stage)
  No forwarding of Sx values!
  Which stage should it be?
    After we read Rx (so WSR can do Rx -> Sx)
    Before we write Rx (so RSR can do Sx -> Rx)
    But not in any stage that gets flushed (can’t undo writes to Sx)!
    So a good stage for this is where we read/write memory (which has the exact same after-read-before-write-can’t-flush issues)

## Slide 42: Jumping to the Interrupt Handler
Option 1: Extend PC selection
Option 2: Treat like a branch misprediction
  If intreq is active, IHA goes into pcgood
Which one to use?
  Option 1 keeps the pcgood computation simpler!
  But Option 2 less likely to affect clock cycle time...
always @(posedge clk) if(lock) begin
if(init) PC<=16'h200;
else if(intreq) PC<=IHA;
else if(mispred_B) PC<=PCcorr_B;
else if(!stall_F) PC<=PCpred_F;
end

## Slide 43: Interrupt Priority?
Make a priority encoder
Put this in IDN when taking interrupt
wire [3:0] intnum=
intr_timer ? 4'h1:
intr_keys ? 4'h2:
intr_sws ? 4'h3:
4'hF;

## Slide 44: When to take the interrupt?
Be careful with stages
  Which stage writes PCS, IRA, etc.?
    Should be the same stage for WSR and int-taking writes
    Must be after we read normal regs (so WSR can work)
    Must be after the inst is “safe” from flushes, otherwise we can get IRA from an inst that was not supposed to execute at all!
  Which stage reads PCS, IRA, etc. in RSR?
    Must be before last stage (so RSR can work)
    Much easier if it’s the same stage where they are written (so we don’t have dependences/hazards between RSR and WSR)
wire intreq= (!reset)&&
(PCS[0]&&(intr_timer||intr_keys||intr_sws)))

## Slide 45: Special Registers - Implementation
As a register file
  Good: Read/Write (RSR, WSR) similar to R* registers
  Bad: On int, need to read/write several of these at once
    Will result in many-ported register file (slow and expensive)
As a bunch of named registers
  Good: Can use PCS, IDN, etc. as needed for Rd/Wr
  Bad: RSR, WSR require a case statement
    Not too bad, “case(sregno)” and update each if its number is selected
Either way, must carefully resolve conflicting r/w
  E.g. check PCS[0] for IE while WSR writing 0 to IE
    If intreq is 1, do we take interrupt here or not?

## Slide 46: Register numbers and forwarding
For RSR, use rregno1 as src register number?
  OK, but make sure it does not mess up forwarding!
  If forwarding based only on rregno, will forward from ADDI R1,R2,R2 to RSR R3,IHA
    This forwarding is wrong and it should not happen
    Note that IHA is the system register 1
  Will need rdrreg1 (read regular register) , rdsreg1 signals (read system register)
    To tell us which register the rregno1 refers to

## Slide 47: Project 4
Implement I/O devices in this new way
  Control/Status regs, timer device, etc.
  Interrupt support is optional in Project 4
    For now your devices can have the IE always set to 0 (no int)
    And you don’t have to have RSR, WSR, and RETI instructions
Write an application, xmax.a32 and xmax.mif
  Implements the LED blinking from Project 1 using our processor
    It must all be implemented as assembler code for our processor, i.e. do not implement the processor as Verilog code from Project 1