## Slide 1: CS3220 Processor Design
Spring 2017
Prof. Hyesoon Kim

## Slide 2: Using FPGA for the AI Chips
This year’s KEYNOTE

## Slide 3: Timing optimizations
You are allowed to do timing optimizations by changing PLL
No “negative slack”
  Even if your results show the correct output, with a negative slack, you will loose point (5 points)

## Slide 4: PLL setups
Use IP Core catalog

## Slide 5: Set filelname  your new pll module name

## Slide 6: Configure output freq.
You can also control duty cycle!
If you use the both edge..
Reg write & read
Save & Ext
Check the box to include the files into your project directory

## Slide 7: Change pll  your new file name

## Slide 8: Use TimeQuest to do clock analysis

## Slide 9: Clock Skew/Clock Delay
Just like data are delayed, clocks can be delayed to.
clk

## Slide 10: Review: Setup Time (Tsu)/Hold Time (TH)
Setup Time: the amount of time the synchronous input (D) must be stable before the active edge of the clock
Hold Time: the amount of time the synchronous input (D) must be stable after the active edge of the clock
If either is violated correct operation of the FF is not guaranteed
CLK
T setup
T hold
stable

## Slide 11: T clk->Q (Clock-to-output delay (tco))
T clk->Q : the amount of time you have to wait after the CLK before the output (Q) is valid
If you try to use the output before this you will get inconsistent results depending on if Q changes
CLK
T setup
stable
T hold
Q Stable
New Q Stable
T clk->Q

## Slide 12: FMAX
Pin-to-Pin Delay (TPD):the time required for a signal from an input pin to propagate through combinational logic and appear at an external output pin.
FMAX: Maximum Clock Frequency: the fastest speed w/o timing violation.
Slack : margin whether a timing requirement is met or not
Slack = required clock period - Actual clock period

## Slide 13: Caution!
If you change your PLL, you have to adjust the counter for the timer

## Slide 14: Writing XMAX.ASM
Writing ASM will take quite a long time than what you think. (>10 hours)
Don’t procrastinate the work.
If your assembler is not robust, your ASM might have bugs which will be very hard to debug with your hardware

## Slide 15: Example of checking KEY status
Loopbegin:
LW S0,KCTRL(Zero) ;Load Current key control bits
ANDI S0,S0,1 ; get KCTRL[0] only
ADDI S1,Zero,1 ; S1 = 1’b1;
BNE S0,S1,CheckSwitches ;Skip key check subroutine if not ready
CALL KeySubroutine(Zero) ;jump to the key subroutine since ready bit is 1

## Slide 16
KeySubroutine:
LW T1,KDATA(Zero) ;Read current key values
ADDI T0,Zero,1 ; T=
BEQ T1,Zero,IncBNLINK ;KEY[1] has been pressed, so increment blinkspeed
…
Q. Do we clear KCTRL [0] bit? Since we read ready bit?

## Slide 17
Set up:
  Timer
  Display initial HEX value (2)
  Setup blankspeed,
  Infinite Loop {
    Check whether time is passed then call time check loop
    Check key is changed
    Check sw is changed
    Loop back
  }

## Slide 18: Running out of Registers!!
We don’t have many registers to work with
  T0, t1, s0..s0. a0-a2 …
Multiple states to keep track
  Blankspeed
  State of lights …
  You have to store them in a memory location and use LD/SW to change them.